## Slide 1: Process Planning and Concurrent Engineering

## Slide 2: Contents
1. Process Planning
2. Computer-Aided Process Planning
3. Concurrent Engineering and Design for Manufacturing
4. Advanced Manufacturing Planning

## Slide 3: Process Planning
“Determining the most appropriate manufacturing processes and the sequence in which they should be performed to produce a given part or product specified by design engineering”
􀂃 Limitations imposed by available processing equipment and productive capacity of the factory must be considered
􀂃 Parts or subassemblies that cannot be made internally must be purchased from external suppliers

## Slide 4: Who does Process Planning?
􀂃 Traditionally, process planning is accomplished by manufacturing engineers who (experts) are familiar with the particular processes in the factory and are able to read engineering drawings
􀂃 Based on their knowledge, skill, and experience, they develop the processing steps in the most logical sequence required to make each part
􀂃 Some details are often delegated to specialists, such as tool designers

## Slide 5: Decisions & Details involved in Process Planning
Interpretation of design drawings
􀂃 The part or product design must be analyzed to begin the process planning procedure
  􀂃 Starting materials
  􀂃 Dimensions
  􀂃 Tolerances
Processes and sequence
􀂃 The process plan should briefly describe all processing steps used to produce the work unit and the order in which they will be performed

## Slide 6: More Decisions & Details in Process Planning
Equipment selection
􀂃 The process planner attempts to develop process plans that utilize existing plant equipment
  􀂃 Otherwise, the part must be purchased, or new equipment must be installed in the plant
Tools, dies, molds, fixtures, and gages
􀂃 Design of special tooling is usually delegated to the tool design group, and fabrication is accomplished by the tool room

## Slide 7: More Decisions & Details in Process Planning
Methods analysis
􀂃 Hand and body motions, workplace layout, small tools, hoists for lifting heavy parts
􀂃 Methods must be specified for manual operations (e.g., assembly) and manual portions of machine cycles (e.g., loading and unloading a production machine)
Work standards
􀂃 Time standards set by work measurement techniques
Cutting tools and cutting conditions for machining operations

## Slide 8: Process Planning for Parts
Processes needed to manufacture a given part are determined largely by the material out of which the part is made and the part design itself
􀂃 The material is selected by the product designer based on functional requirements
􀂃 Once the material has been selected, the choice of possible processes is narrowed considerably

## Slide 9: Typical Processing Sequence
A typical processing sequence to fabricate a discrete part consists of
1. A basic process
2. One or more secondary processes
3. Operations to enhance physical properties
4. Finishing operations

## Slide 10: Basic and Secondary Operations
Basic process
􀂃 Establishes initial geometry of workpart
  􀂃 Examples: metal casting, forging, sheet metal rolling
Secondary processes
􀂃 In most cases, the starting geometry must be modified or refined by a series of secondary processes, which transform the basic shape into the final geometry
  􀂃 Examples: machining, stamping

## Slide 11: Property Enhancement and Finishing Operations
Operations to enhance properties
􀂃 Heat treatment operations
  􀂃 Treatments to strengthen metal components
  􀂃In many cases, parts do not require these property enhancing steps
Finishing operations
􀂃 The final operations in the sequence
􀂃 Usually provide a coating on the work surface
  􀂃 Examples: electroplating, painting

## Slide 12: Examples of Typical Process Sequences

## Slide 13: Process Planning: Basic Process
􀂃 Process planning usually begins after the basic process has provided initial part shape
  􀂃 Example: machined parts begin as bar stock or castings or forgings, and these basic processes are often external to the fabricating plant
  􀂃 Example: stampings begin as sheet metal coils or strips purchased from the mill
􀂃 These are the raw materials supplied from external suppliers for the secondary processes performed in the factory

## Slide 14: The Route Sheet
“The document that specifies the details of the process plan”
􀂃 The route sheet is to the process planner what the engineering drawing is to the product designer
􀂃 Route sheet should include all manufacturing operations to be performed on the workpart, listed in the order in which they are to be performed

## Slide 15: Route Sheet for Process Planning
the processing sequence is documented on the route sheet

## Slide 16: Process Planning for Assemblies
􀂃 For single stations, the documentation contains a list of the assembly steps in the order in which they must be accomplished
􀂃 For assembly line production, process planning consists of line balancing - allocating work elements to particular stations along the line
􀂃 As with process planning for individual parts, any tools and fixtures needed to accomplish a given assembly task must be decided, and the workplace layout must be designed

## Slide 17: Make or Buy Decision
􀂃 Inevitably, the question arises whether a given part should be purchased from an outside vendor or made internally
􀂃 Virtually all manufacturers purchase their starting materials from suppliers
􀂃 Very few production operations are vertically integrated all the way from raw materials to finished product
􀂃 The make versus buy question is probably appropriate to ask for every component used by the company

## Slide 18: Make or Buy Example
Given: The quoted part price from a vendor = $20.00 per unit for 100 units. The same part made in the home factory would cost $28.00. Cost breakdown on the make alternative is as follows:
Unit material cost = $8.00 per unit
Direct labor = $6.00 per unit
Labor overhead at 150% = $9.00 per unit
Equipment fixed cost = $5.00 per unit
Total = $28.00 per unit
􀂃 Should the component be bought or made in-house?

## Slide 19: Make or Buy Example - continued
Although the vendor's quote seems to favor the buy decision, consider the possible effect on the factory if the quote is accepted
􀂃 Equipment fixed cost of $5.00 is an allocated cost based on an investment that has already been made
􀂃 If equipment is idled by a buy decision, then the fixed cost continues even if the equipment is not in use
􀂃 Overhead cost of $9.00 consists of factory floor space, indirect labor, and other costs that will also continue even if the part is bought

## Slide 20: Make or Buy Example - continued
􀂃 By this reasoning, the decision to purchase might cost the company as much as $20.00 + $5.00 + $9.00 = $34.00 per unit if it results in idle time in the factory on the machine that would have been used to make the part
􀂃 On the other hand, if the equipment can be used to produce other components for which the internal prices are less than the corresponding external quotes, then a buy decision makes good economic sense

## Slide 21: Computer-Aided Process Planning
􀂃 During the last several decades, there has been considerable interest in automating the process planning function by computer systems
􀂃 Shop people knowledgeable in manufacturing processes are gradually retiring
􀂃 An alternative approach to process planning is needed, and computer-aided process planning (CAPP) provides this alternative

## Slide 22: Benefits of CAPP
􀂃 Process rationalization and standardization
  􀂃 CAPP leads to more logical and consistent process plans than traditional process planning
􀂃 Increased productivity of process planners
􀂃 Reduced lead time to prepare process plans
􀂃 Improved legibility over manually written route sheets
􀂃 Incorporation of other application programs
  􀂃 CAPP programs can be interfaced with other application programs, such as cost estimating, work standards, and NC part programming

## Slide 23: CAPP Systems
Computer-aided process planning systems are designed
around either of two approaches:
1. Retrieval systems
2. Generative systems

## Slide 24: Retrieval CAPP Systems
􀂃 Based on group technology and parts classification and coding
􀂃 A standard process plan is stored in computer files for each part code number
  􀂃 The standard plans are based on current part routings in use in the factory, or on an ideal plan prepared for each family
  􀂃 For each new part, the standard plan is edited if modifications are needed
􀂃 Also known as variant CAPP systems

## Slide 25: Retrieval CAPP System
Operation of a retrieval type computer-aided process planning system

## Slide 26: Retrieval CAPP Systems - continued
􀂃 If the file does not contain a standard process plan for the given code number, the user may search the file for a similar code number
  􀂃 By editing an existing process plan, or starting from scratch, the user develops a new process plan that becomes the standard plan for the new part code
􀂃 Final step is the process plan formatter
  􀂃 Formatter may call other application programs: determining cutting conditions, calculating standard times, or computing cost estimates

## Slide 27: Generative CAPP Systems
Rather than retrieving and editing an existing plan from a data base, the process plan is created using systematic procedures that might be applied by a human planner
􀂃 In a fully generative CAPP system, the process sequence is planned without human assistance and without predefined standard plans
􀂃 Designing a generative CAPP system is a problem in expert systems
  􀂃 Computer programs capable of solving complex problems that normally require a human with years of education and experience

## Slide 28: Components of an Expert System
􀂃 Knowledge base
  􀂃 The technical knowledge of manufacturing and logic used by process planners must be captured and coded in a computer program
􀂃 Computer-compatible part description
  􀂃 The description must contain all the pertinent data needed to plan the process sequence
􀂃 Inference engine
  􀂃 The algorithm that applies the planning logic and process knowledge contained in the knowledge base to a given part description