Mid Term Spring 2015 (BSc. Engg) Industrial Engineering Department, UET, Taxila

(ME 294) Mechanics of Materials

Time Allowed: (8 minutes for MCQs)						      Max. Marks: 20

(Encircle your Choices) and Solve Question 1 on this sheet and Return to Invigilation Staff after 10 minutes.

Name: ___________________________________	Regd No: ___________________

Question 1(5):

- In Mechanics of Materials, we keep the following  assumption/assumptions

- Rigid				b) Equilibrium

- Equilibrium and Rigid		d) All of the above

- 1 MPa = ..........

- 1 N/m2				b) 1kN/mm2        c)1 N/mm2 		d) None of the above

- The symbol for normal strain is ………….

- ɣ		b) σ		c) τ		d) ε

- The thermal stress does not depend on the……………………. of the bar.

- length 	      b) co-efficient of thermal expansion   c) modulus of elasticity     d) temperature change

- Shear stress acts ……………. to the surface.

- Perpendicular		b) Parallel	c) both a and b 	d) None of them

- Many manufacturing operations on metals are performed at stress levels between the …………..and the tensile strength.

- Yield Strength		b) UTS		c) Fracture strength		d) Fatigue strength

- Structures are classified as statically determinate if  their reactions and internal forces can be determined solely from

- free-body diagrams 	b) equations of equilibriums	c) equations of compatibility	d) Both a and b

- Young’s modulus, E, is the slope of the stress-strain curve ……..the test specimen starts to yield

- before			b) after		c) both a and b 		d) None of them

- The strain  is uniform upto…………..

a) Yield Strength		b) UTS		c) Fracture strength		d) Fatigue strength

- Factors of safety with respect to the ultimate strength of a material are usually ……… than those based upon yield strength.

- Smaller			b) Larger		c) same		d) None of them

Mid Term Exam (BSc. Engg) Industrial Engineering Department, UET, Taxila

(ME 294) Mechanics of Materials

Part B

Note: No Choice, Assume any data where necessary, Solve Part B on the ANSWER BOOK

Time Allowed: 1:30 minutes

Question No 2 (4):

Determine the total increase of length of a bar of constant cross section (A) hanging vertically and subject to its own weight as the only load. Assume: Length of bar is L , young’ modulus is E and specific weight of bar is ɣ. The elongation of the element of thickness dy shown is                    where W denotes the total weight of the bar.

Question No 3 (4):

Define the following:Complementary Shear Stress : A shear stress is always accompanied by a balancing shear stress across the planes at right angles, the balancing stress is called complementary shearing stress.

- Bulk Modulus  : Bulk Modulus or Volume Modulus of elasticity:It is defined as the ratio of applied pressure (on each face of solid cube) to volumetric strain. It is represented by ‘K’ K = p/εv

c)   Modulus of elasticity: It is the ratio between compressive stress and compressive strain or tensile stress and tensile strain. It is denoted by ‘E’

      - E = stress/stain = σ/ε = σt/εt = σc/εc

d) Modulus of rigidity: Modulus of rigidity or shear modulus :It is the ratio of shear stress (τ) to shear strain (γ). It is represented by ‘C’, ‘N’ or ‘G’.

      - C, N or G = τ/γ

Question No 4 (3):

A 3 mm thick aluminum sheet is cut with a 4 cm diameter round punch. If the punch exerts a force of 6 kN, what is the shear stress in the sheet?

The area equals the circumference of the circle times the thickness of the sheet metal: A=πdt.

Shear stress τ= P/ A

=P/ πdt= 6kN/π⋅4cm⋅3mm =15.9MPa

Question No 5 (4):

The prismatic bar AB is attached to rigid supports at both ends and is axially loaded by a force P at an intermediate point C. Find the reactions RA and RB .

- These forces cause the bar to change in length by an amount δ AB , which must be equal to zero:

δ AB = 0 ………..(b)    This equation, called an equation of compatibility