CCN				Assignment 03	10 Marks		 24 Mar 09

Due Date: March 31, 2009

In case of any query: waleed.ejaz@uettaxila.edu.pk

Problem 1

(a) An application has the following bit pattern to transmit over a Stop and Wait communications link:

1 0 0 1 0 0 1 1 0 1 1 0

What would be the data bits sent over the communication channel if the data link used a cyclic redundancy check with a generator polynomial of the form:

P(x) = x3 + 1

(b) If the bits that arrived at the receiver for the above transmission had the following bit pattern:

1 0 0 1 0 0 1 1 0 1 1 1 0 0 1

What would be the response of the receiver?

Problem 2

(a) Compute the checksum for the following data bits:
11010100 11001001 11011001 00001001
Assume an 8 bit checksum is being used.

(b) if bits 6 and 22 (counting from the left starting at 1) arrived in error, what would be the reaction at the receiver?

Problem 3
(a) Assume a Sliding Window with Go-Back N ARQ is being used on a transmission link with a window size of 7 (window includes frames numbers 0 through 6). The transmitter has previously sent frames 0, 1 and 2. Is the transmitter allowed to send frame 3 if frame 2 has not been acknowledged? Explain your answer.

(b) Assume a Sliding Window with Go-Back N ARQ is being used on a transmission link with a window size of 7 (window includes frames numbers 0 through 6).

- If the transmitter sends frames 0, 1, 2 and 3 what is the size of the send window?

- If the receiver sends back ACK 2, what is the new size of the send window? What frame numbers are in the send window?

(c) Assume a Sliding Window with Selective-Reject ARQ is being used on a transmission link with a window size of 8 (transmit and receive window includes frames numbers 0 through 7). Host A sends frames 0, 1, 2, 3, and 4 to the receiver and frame 3 is received in error by Host B.

- What is the size of the receive window at Host B?

- What would be the frame number in the ACK sent back by Host B?

Problem 4

Given a (15,11) Hamming code with the redundant bits defined as follows:

b 1 = b 3 + b 5 + b 7 + b 9 + b11 + b13 + b15
b 2 = b 3 + b 6 + b 7 + b10+ b11 + b14 + b15
b 4 = b 5 + b 6 + b 7 + b12+ b13 + b14 + b15
b 8 = b 9 + b10+ b11+ b12+ b13 + b14 + b15

(a) Calculate the transmitted code word for the following message:

3  5  6  7  9 10 11 12 13 14 15  (bit position)

0  0  1  0  0  0  1  0  0  1  0

(b) What would be the error code word at the receiver if bit 14 arrives in error (i.e. bit 14 = 0).

Problem 5

Why there is a lower limit on payload length? Is this because of CSMA/CD? If yes then prove why it is 46 bytes?

Chapter 11 (BF) Exercises

8, 9, 21, 23, 25, 28, 29, 30